## Slide 1
HT-MFG2 Mold Equipment Budget Request
1

## Slide 2
HT-MFG2 Mold Equipment Budget Request
2

## Slide 3
61J
62J
63J
64J
J608
41S
42S
43S
44S
45S
32S
33J
301S
184N
Cover Protect dust
Store part
313S
37J
38J
39J
53J
J515
J516
54J
49J
410J
411J
211J
210J
29J
28J
27J
Die Keep area
Die Keep area
64m2
52m2
103S
501J
182S
22S
24S
21S
185J
Move Shell Die Keep
54m2
2nd PAD
54m2
2nd Screen
60m2
101S
R
4
Move Shell Die Keep
60m2
Store part
R
1
104S
R
5
R
3
R
6
181S
R
2
MP Line 06B | MC Total | Man Use | Die Space | 2nd Pad+Scr Space | 2nd Weld+ Check Space | KD Space
Line :1 | 10 | 8*2 | 362 | 89.8 | 119.2 | 32.0
Line :2 | 14 | 8*2 |  |  |  | 
Line :3 | 11 | 7*2 |  |  |  | 
Line :4 | 14 | 7*2 |  |  |  | 
Total | 49 | 60 | M2 | TLL 2nd =241M2 |  | 
 Layout Mold Production (06-Building)
MC Size Ton | Act. Oct'25 | Plan Jan’26 | Plan Apr’26 | Plan Jun’26
1000T | 2 | 2 | 2 | 2
650T | 5 | 7 | 9 | 9
550T | 2 | 5 | 7 | 7
450T | 8 | 8 | 8 | 8
350T | 9 | 9 | 9 | 6
220T | 10 | 10 | 10 | 8
180T | 3 | 3 | 3 | 3
100T | 3 | 3 | 3 | 3
102 (Gear) | 1 | 1 | 1 | 0
50T (Casset) | 2 | 2 | 2 | 1
184 (Gear) | 1 | 1 | 1 | 1
301 (Gear) | 1 | 1 | 1 | 1
TLL MC Use | 47 | 52 | 56 | 49
MC Sell TLL=7MC
Merit: After MC Sell
& Re-lay out
Man Reduce=5Per.
Free Spec =331M2
J602
MC Re-Lay out TLL=6MC
D
D
D
D
D
D
D
D
D
D
D
D
Mat’l auto loading
【 Ideal of MFG2 Full Automation Combine Cell】
68J
J607
J606
1001J
1002J
J512
J514
J513
44S
42S
43S
41S
J606
43S
64J
62J
63J
61J

## Slide 4
HT-MFG2 Mold Equipment Budget Request
4
【 Aru Beki Re-Lay out mold 06 building 】
MP Line 06B | MC Total | Man Use | Die Space | 2nd Pad+Scr Space | 2nd Weld+ Check Space | KD Space
Line :1 | 10 | 8*2 | 362 | 89.8 | 119.2 | 32.0
Line :2 | 14 | 8*2 |  |  |  | 
Line :3 | 11 | 7*2 |  |  |  | 
Line :4 | 14 | 7*2 |  |  |  | 
Total | 49 | 60 | M2 | TLL 2nd =241M2 |  | 
Capacity MC JunY26 (49MC)
MC Size Ton | Act. Oct'25 | Plan Jan’26 | Plan Apr’26 | Plan Jun’26
1000T | 2 | 2 | 2 | 2
650T | 5 | 7 | 9 | 9
550T | 2 | 5 | 7 | 7
450T | 8 | 8 | 8 | 8
350T | 9 | 9 | 9 | 6
220T | 10 | 10 | 10 | 8
180T | 3 | 3 | 3 | 3
100T | 3 | 3 | 3 | 3
102 (Gear) | 1 | 1 | 1 | 0
50T (Casset) | 2 | 2 | 2 | 1
184 (Gear) | 1 | 1 | 1 | 1
301 (Gear) | 1 | 1 | 1 | 1
TLL MC Use | 47 | 52 | 56 | 49
MC Sell TLL=7MC
Merit: After MC Sell
& Re-lay out
Man Reduce=5Per.
Free Spec =331M2
MC Re-Lay out TLL=6MC
Machine 1001J , 1002J

## Slide 5
HT-MFG2 2nd Half Action Plan Review : Engineering
5
Target : Machine 1000 Ton (1001T , 1002T)
Full auto production combine cell
 | Process MC | Work Process / Manpower |  |  |  |  |  |  | Manpower total | 
 |  | Cut gat | Pad Screen | Cut bari | Clean oil | ASSY part | Final check | Packing |  | 
Current | MC-1001T | 1 P. |  |  |  | 1 P. |  |  | 2 P. | 4 P.
 | MC-1002T | 1 P. |  |  |  | 1 P |  |  | 2 P. | 
After Improve | MC-1001T | Automation |  | 0.7 P. |  |  | Automation | 1 P. | 3 P. | 
 | MC-1002T | Automation |  | 0.7 P. |  |  | Automation |  |  | 
 |  |  |  | Katsu-JIN = 0.6 |  |  |  |  | Sho-JIN=1 P. | 
Summary Merit | 
Equipment Budget | 1,500 KB
Manpower Reduction | 1.6 P./Shift x 2 Shift = 3.2 Person
ROI | = 0.5 (23 month)
Current :
Improve : Automation
Automation
Set No.1
Support 2 Parts
Automation
Set No.1
Support 21 Parts
Add Automation
Set No.2
Support 29 Parts
Add Conveyor
To combine
1001T & 1002T
Packing 1 P.
4
3
2
1
1
2
3

## Slide 6
 |  | Process |  |  |  |  |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  | 
 |  | Cut Gate | Cut Bari | Wipe off oil stains | Assembly Rubber Foot | Drain Sheet | PAD | Appearance Check | Packing (3 Type) |  | 
 |  |  |  |  |  |  |  |  | Box | Box + Bage | Rack
MC 1001 | Man1 |  |  |  |  |  |  |  |  |  | 
 | Man2 |  |  |  |  |  |  |  |  |  | 
MC 1002 | Man3 |  |  |  |  |  |  |  |  |  | 
 | Man4 |  |  |  |  |  |  |  |  |  | 
After |  | Automation -Robot | Man | Man | Automation -Robot | Man | Automation -Robot | Automation -Robot -Camera | Man | Man | Man
 |  |  |  |  |  |  |  |  | Conveyor Combine 1001T + 1002T |  | 
 1001T and 1002T Production Process & Manpower Workload
HT-MFG2 Mold Equipment Budget Request
6
 | Total part list (Item part) | Production (part / day) | Manpower (Person)
MC 1001 | 21 | XX | 2
MC 1002 | 29 | XX | 2

## Slide 7
HT-MFG2 Mold Equipment Budget Request
7
 Workload Balance & Manpower Sho-JIN / Katsu-JIN
Unit : Process
Chart: 
| Man1 | Man2 | Camera | Robot | Man3 | Man4 | Camera | Robot | M/C 1001 | M/C 1002
Process | 4 | 4 | 3 | 3 | 3 | 3 | 0 | 0
(Sho-Jin Manpower 4 = 1 by Mold Auto production)
Chart: 
| Man1 | Man2 | Camera | Robot | Man3 | Man4 | Camera | Robot | M/C 1001 | M/C 1002
Before | 4 | 4 | 3 | 3 | 3 | 3 | 0 | 0
After | 3 | 4 | 3 | 4 | 1 | 0 | 3 | 3
Unit : Process
( Auto production)

## Slide 8
Summary Process machine 1000Ton after “Mold Auto-Production” |  |  |  |  |  |  |  | 
Process | Cutting gate | Cut Bari | Cleaning Oil | PAD Printing | Assembly Rubber Foot | Drain Sheet | Appearance Check | Packing
Man1 | O | O | O | X | X | X | X | X
Man2 | O | O | O | X | X | O | X | X
Man3 | X | X | X | X | X | X | X | O
Robot | O | X | X | O | O | X | O | X
Camera | O | X | X | O | X | X | O | X
HT-MFG2 Mold Equipment Budget Request
8
Project Name : Mold Auto-Production
Man-2
Man-1
Man-3
-Auto-Cutting Gate
-Auto PAD
-Auto Camera CHK
1.Modify Auto Set #1.
to cover all part
2.Add Auto Set #2.
3.Add Conveyor u.
Combine
2 MC.
-Auto AGV
 Concept manpower and machine Size 1000 Ton
-Auto-Cutting Gate
-Auto PAD
-Auto Camera CHK
 Number of working processes of machines and man
(Sho-Jin Manpower 4 = 1 by Mold Auto production)
 Process Machine 1000 Ton
Detail change point
1.Modify Auto Set #1.to cover all part
2.Add Auto Set #2.
3.Add Conveyor u Combine 2 MC.
Chart: 
| Man1 | Man2 | Camera | Robot | Man3 | Man4 | Camera | Robot | M/C 1001 | M/C 1002
Before | 4 | 4 | 3 | 3 | 3 | 3 | 0 | 0
After | 3 | 4 | 3 | 4 | 1 | 0 | 3 | 3
Unit : Process
Condition : O =Yes X = No
( Auto production)

## Slide 9
HT-MFG2 Mold Equipment Budget Request
9
1.Auto Cut Gate
1.Auto Cut Gate
2.PAD
3.CAMERA CHECK
2.CAMERA CHECK
ROBOT
ROBOT
(Wait Transfer Form CHT-RA)
1001J
1002J
AGV
AGV
1.Operator Confirm Part
2.Operator Confirm Part
3.Operator for Packing Part To Box and Control AGV Auto To Store Part
Robot Move Cutting Gate Part
Part Have Process PAD Robot Move To PAD
CAMERA CHECK
Operator Confirm Part
Operator Packing
Robot Move Cutting Gate Part
CAMERA CHECK
Operator Confirm Part
Operator Packing
1
2
3
4
5
1
2
3
4
Project Name : Mold Auto-Production
 Detail Automation Concept

## Slide 10
HT-MFG2 Mold Equipment Budget Request
10
1.Auto Cut Gate
2.CAMERA CHECK
ROBOT
(Wait Transfer Form CHT-RA)
1001J
1002J
AGV
AGV
1.Operator Confirm Part
2.Operator Confirm Part
3.Operator for Packing Part To Box and Control AGV Auto To Store Part
Robot Move Cutting Gate Part
Part Have Process PAD Robot Move To PAD
CAMERA CHECK
Operator Confirm Part
Operator Packing
Robot Move Cutting Gate Part
CAMERA CHECK
Operator Confirm Part
Operator Packing
1
2
3
4
5
1
2
3
4
Project Name : Mold Auto-Production
 Detail Automation Concept
Gate Cutting
PAD/Screen
Appearance Check

## Slide 11
HT-MFG2 Mold Equipment Budget Request
11
Flow การทำงาน
เลือกและ Start: ผู้ใช้เลือกคำสั่งบนจอ HMI แล้วกด Start
PLC สั่ง Robot: PLC รับคำสั่งและส่งไปให้ Robot
Robot ทำงานทีละ Process:
  - ตัด Gate: Robot ไปที่จุดตัด, สั่ง Air Nipper ตัด
  - Pad: Robot ไปที่จุด PAD , สั่งเครื่อง Pad
  - ตรวจสอบ: Robot ไปที่จุดตรวจสอบ, สั่งกล้อง IV4 ทั้งสองตัวตรวจสอบ
Robot รายงานผล: Robot ส่งผลการทำงานแต่ละขั้นกลับไปที่ PLC
PLC อัปเดต HMI: PLC แจ้งสถานะการทำงานทั้งหมดกลับไปที่ HMI
ทั้งหมดนี้จะสื่อสารกันผ่านระบบ CC-Link เพื่อให้ข้อมูลไหลเวียนได้อย่างรวดเร็วและมีประสิทธิภาพ
New Concept
Gate
PAD
CHECK
Send
CC-Link

## Slide 12
HT-MFG2 Mold Equipment Budget Request
12
No. | KEYENCE IV4 Series | Cognex In-Sight 2000 Series (Closest Competitor) | Omron FQ2 Series (Alternative Competitor)
Main Product Type | Vision Sensor (with built-in AI) | Vision Sensor / Smart Camera | Vision Sensor
Key Technology | AI Accelerator Chip and Built-in Deep Learning/AI | Rule-based Vision Tools (Pattern, Edge, Blob) | Rule-based and Algorithmic Vision Tools
Resolution | Approx. 1.2 MP (1/2.9 inch CMOS) | Up to 1.3 MP | Up to 1.3 MP
Processing Speed | Up to 250 parts/sec (4 ms.) for AI judgment | Medium to High (depending on tool complexity) | Medium to High
Installation | All-in-one (Camera, Lens, Lighting) | All-in-one (Camera, Lens, Lighting) | All-in-one (Camera, Lens, Lighting)
Ease of Setup | Very Easy (Uses only a few sample images to train AI, no position adjustment needed) | Easy (Uses Spreadsheet Interface/GUI) | Easy to use with HMI or PC Software
IV4 Strengths | High inspection stability, even with slight variations in workpiece position or surface (AI Differentiate, AI Identify) | Features highly accurate vision tools (Padma Redline) and has a wide industrial customer base | Highly reliable in production lines and easily connects to Omron PLCs
Price Level (Estimated) | High (Premium, focused on AI innovation and simplicity) | Medium to High (depending on sub-model) | Medium to High
Vision Sensor Industry Comparison Table (IV4 Series)
2.Camera Unit

## Slide 13
HT-MFG2 Mold Equipment Budget Request
13
2.Camera Unit
2. Camera Unit |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Camera (IV 4 KEYENCE) | 110 | 3 | 330
2 | Structure and Cover | 30 | 1 | 30
Total Cost |  |  |  | 360
Black Dot
Check Confirm PAD
Concept Robot Move part use Camera check
Box Camera

## Slide 14
HT-MFG2 Mold Equipment Budget Request
14
1.Automation Cut Gate
ROBOT
Injection Machine
PART
PART
Function
Step of Automation Cut Gate
Robot of machine injection input Part at table automation cut gate
Robot 7 axis move part to Auto Nipper at position gate at part
Estimate Time = 5-10 Sec.
1. Auto Cutting Unit |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Air Nipper | 20 | 2 | 40
2 | Sensor Check | 15 | 2 | 30
3 | Solenoid Valve | 3 | 3 | 9
4 | Structure and Cover | 11 | 1 | 11
Total Cost |  |  |  | 90
Jig Move Air Nipper depend on Shape part on

## Slide 15
HT-MFG2 Mold Equipment Budget Request
15
Conveyor Unit
Length 5.5 M
Detail order part Conveyor Unit |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | AC Motor | 5 | 4 | 20
2 | Belt Conveyor | 10 | 4 | 40
3 | Structure Conveyor | 20 | 1 | 20
Total Cost |  |  |  | 80
Motor
Belt
Aluminum Profile
Roller
Assembly By CHT-MOLD
0.7 M
0.7 M
1.5 M
Unit Price (In case of order)
Unit Price : 1 set length 1.2 meters price 265,405 baht
 1 set of Estimate Cost 80,000 baht
Conveyor
 Detail Conveyor
Check price from Misumi
“Select Concept 2 of buying some parts to assemble internally to reduce costs”.
Length 5.5 M
Length 9.5 M
 Concept 1 .Ready-made order.
 Concept 2. Ordering some parts.

## Slide 16
HT-MFG2 Mold Equipment Budget Request
16
Electrical Equipment Unit
4. Electrical Equipment |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Box Control | 13 | 1 | 13
2 | PLC MELSEC-F FX3S | 40 | 1 | 40
3 | GOT2000 Series GT21 | 27 | 1 | 27
4 | Power Support | 10 | 1 | 10
Total Cost |  |  |  | 90

## Slide 17
Robot
Conveyor Unit
Conveyor Unit
Camera Unit
1.Auto-Cutting Gate
2.Auto-PAD Printing
3.Auto-Appearance CHK by Camera
4.Auto-Packing by Robot
1. Auto Cutting Unit |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Air Nipper | 20 | 2 | 40
2 | Sensor Check | 15 | 2 | 30
3 | Solenoid Valve | 3 | 3 | 9
4 | Structure and Cover | 11 | 1 | 11
Total Cost |  |  |  | 90
2. Camera Unit |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Camera (IV 4 KEYENCE) | 110 | 3 | 330
2 | Structure and Cover | 30 | 1 | 30
Total Cost |  |  |  | 360
3. Conveyor Unit |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | AC Motor | 5 | 4 | 20
2 | Belt Conveyor | 10 | 4 | 40
3 | Structure Conveyor | 20 | 1 | 20
Total Cost |  |  |  | 80
4. Electrical Equipment |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Box Control | 13 | 1 | 13
2 | PLC MELSEC-F FX3S | 40 | 1 | 40
3 | GOT2000 Series GT21 | 27 | 1 | 27
4 | Power Support | 10 | 1 | 10
Total Cost |  |  |  | 90
5. Cover Unit |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Area Sensor | 40 | 1 | 40
2 | Structure and Cover | 20 | 1 | 20
Total Cost |  |  |  | 60
6. Gripper Robot |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Cylinder Gipper | 35 | 1 | 35
2 | Structure and Cover | 5 | 1 | 5
Total Cost |  |  |  | 40
Detail : Equipment for Unit in Projection Auto Production Step 2
Man-2
Man-1
Man-3
-Auto-Cutting Gate
-Auto PAD
-Auto-Cutting Gate
-Auto PAD
-Auto Camera CHK
-Auto Camera CHK
1.Modify Auto Set #1.
to cover all part
2.Add Auto Set #2.
3.Add Conveyor u.
Combine
2 MC.
-Auto AGV
Detail Show Cost for Unit by Unit
Sum Detail Unit for 1 Machine Cost = 720 KB.
For Project Auto Production use 2 Machine Cost =1440 KB.
HT-MFG2 Mold Equipment Budget Request
17
 Estimate ROI
1,440 KB. / 3.2 P. x 235 KB. = 1.95 Year (23months)
Notes: เนื่องจากในปีนี้ ทางMFG2 Mold มีแผนการทำProject Full Auto Production
โดยมีเป้าหมายที่เครื่องฉีด1001T
มีProcessการทำงานหลัก 4 ขั้นตอน
Cutting Gate
PAD Printing
Appearance Check
Packing

## Slide 18
Appendix

## Slide 19
Project Name : Mold Auto-Production , Purpose : Cost Down (Sho-JIN / Ktsu-JIN)
 Ktasu-JIN , Sho-Jin |  |  |  |  | 
Process |  | Manpower (Person / Shift) |  |  | 
 |  | Before |  | After | 
 |  | 1001T | 1002T | 1001T | 1002T
1 | Cutting Gate | 1 | 1 | 0.7 Katsu-JIN =0.3 | 0.7 Katsu-JIN =0.3
2 | Cut Bari |  |  |  | 
3 | Cleaning Oil |  |  |  | 
4 | PAD Printing | 1 | 1 |  | 
5 | Appearance Check |  |  | 1 (Sho-Jin = 1) | 
6 | Packing |  |  |  | 
Total |  | 4 |  | 1.4 | 
Reduce Manpower = 1.6 Person / Shift Total 2 Shift = 3.2 Person |  |  |  |  | 
 Estimate Cost |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost / u. | Q’TY | Total Cost
1 | Auto Cutting Unit | 90 | 2 | 180
2 | Camera Check Unit | 300 | 2 | 600
3 | Conveyor Unit | 80 | 2 | 160
4 | Electrical Equipment | 90 | 2 | 180
5 | Cover Unit | 60 | 2 | 120
6 | Gripper Robot | 40 | 2 | 80
Total Cost |  |  |  | 1,440
ASSETS | OBJ. | BUDGET CODE | BUDGET NAME | W.C. | BUDGET (KB.) | ORDER
04 | 30 | 25ZZ04001 | Automation New | 3601 | 1,500 | 10/2025
 Estimate ROI
1,440 KB. / 3.2 P. x 235 KB. = 1.95 Year (23months)
Man-1
Man-2
Man-3
Man-4
-Auto Camera CHK
-Auto-Cutting Gate
-Auto PAD
Before
Man-2
Man-1
Man-3
-Auto-Cutting Gate
-Auto PAD
-Auto-Cutting Gate
-Auto PAD
-Auto Camera CHK
-Auto Camera CHK
1.Modify Auto Set #1.
to cover all part
2.Add Auto Set #2.
3.Add Conveyor u.
Combine
2 MC.
After
-Auto AGV
Auto Set #1.
Support production 2 parts
HT-MFG2 Mold Equipment Budget Request
19
Notes: เนื่องจากในปีนี้ ทางMFG2 Mold มีแผนการทำProject Full Auto Production
โดยมีเป้าหมายที่เครื่องฉีด1001T
มีProcessการทำงานหลัก 4 ขั้นตอน
Cutting Gate
PAD Printing
Appearance Check
Packing

## Slide 20
Cutting gate | Wipe off oil stains | Cut Bari | BOX | Box (มีถุงด้านใน) | Assembly Rubber Foot | Drain Sheet | PAD | Rack | Confirm Part
Part Injection 1001T and 1002T
Process Part All 10 Process
New Process (ROBOT / OPERATOR)
Camera
Compare Process for New Process Add Robot
Camera
Camera
HT-MFG2 Mold Equipment Budget Request
20

## Slide 21
ยกตัวอย่างการการปรับปรุง 1 Case
เลือก Partที่มีMeritสูง QC5-6187 / QC91451
Picture
Before
After
Process Before
Process After
Time chart Before
Time chart Before
Conclude Merit

## Slide 22
Appearance Check Require.. |  | Ability of Camera
Check Item | Judge Method | 
 | Spec XXX | 
 | D/S , Limit Sample | 
ตัวอย่างจุดตรวจสอบยาก และปัญหาการตรวจสอบหรุดรอด
การรองรับด้วยCamera check

## Slide 23
Action Plan / Schedule
Full auto Production Step 2
Action plan process |  | 2025 |  |  |  |  | 2026 |  |  |  |  |  | 
 |  | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul
Design 3D | Plan |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  | 
Request Equipment Budget | Plan |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  | 
Order part | Plan |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  | 
Making | Plan |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  | 
Debug | Plan |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  | 
Input MP | Plan |  |  |  |  |  |  |  |  |  |  |  | 
 | Actual |  |  |  |  |  |  |  |  |  |  |  | 
HT-MFG2 Mold Equipment Budget Request
23
Notes: Action plan

## Slide 24
HT-MFG2 Mold Equipment Budget Request
24
Camera Check Concept.
1. Appearance Guarantee Items / Spec.
2. Equipment SPEC Requirement
3. Camera check design concept
4. Equipment cost / order preparation
-Quotation …
2. Camera Unit |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Camera (IV 4 KEYENCE) | 110 | 3 | 330
2 | Structure and Cover | 30 | 1 | 30
Total Cost |  |  |  | 360
แยกข้อมูลแต่ละUnitให้เข้าใจถึงการออกแบบ การทำงาน ความสามารถ และEquipmentที่ต้องการ (ทุก Unit)

## Slide 25
HT-MFG2 Mold Equipment Budget Request
25
CTRL Box
Robot
Auto PAD
Camera
Auto
Cut
gate
Automation Concept.
ทำFlowให้เข้าใจเส้นทางของPartและการทำงานของเครื่อง คน Robot

## Slide 26
HT-MFG2 Mold Equipment Budget Request
26
Automation Concept.
1.Auto Cut Gate
1.Auto Cut Gate
2.PAD
3.CAMERA CHECK
2.CAMERA CHECK
ROBOT
ROBOT
(Wait Transfer Form CHT-RA)
1001J
1002J
AGV
AGV
4.Operator Confirm Part
3.Operator Confirm Part
Operator for Packing Part To Box and Control AGV Auto To Store Part
Robot Move Cutting Gate Part
Part Have Process PAD Robot Move To PAD
CAMERA CHECK
Operator Confirm Part
Operator Packing
Robot Move Cutting Gate Part
CAMERA CHECK
Operator Confirm Part
Operator Packing
1
2
3
4
5
1
2
3
4
Before
After
1001 J
1002 J
1
2
3
4

## Slide 27
HT-MFG2 Mold Equipment Budget Request
27
Camera Check Concept.
1. Appearance Guarantee Items / Spec.
2. Equipment SPEC Requirement
3. Camera check design concept
4. Equipment cost / order preparation
-Quotation …
2. Camera Unit |  |  |  | 
Equipment Name |  | Estimate Cost (KB.) |  | 
 |  | Cost | Q’TY | Total Cost
1 | Camera (IV 4 KEYENCE) | 110 | 3 | 330
2 | Structure and Cover | 30 | 1 | 30
Total Cost |  |  |  | 360
แยกข้อมูลแต่ละUnitให้เข้าใจถึงการออกแบบ การทำงาน ความสามารถ และEquipmentที่ต้องการ (ทุก Unit)

## Slide 28
 |  |  |  |  | Planner | Production | Qa
No | M / C | Mold Master | Part no |  | Lot size | Man power | Point bari
1 | 1001J | QC8-1089 |  |  | 1 | 1 | 0
2 | 1001J | QC8-1090 |  |  | 2 | 1 | 0
3 | 1001J | QC8-1084 |  |  | 1 | 1 | 2
4 | 1001J | QC8-1086 |  |  | 1 | 1 | 1 (ใย Bari)
5 | 1001J | QC4-7500 |  |  | 1 | 2 | 0
6 | 1001J | QC4-7542 |  |  | 1 | 2 | 0
7 | 1001J | QC6-6991 | QL3-1513(ประกอบdrain sheet&Ruber foot) |  | 1 | 1 | 1
8 | 1001J | QC5-2640 | QC8-5521(change mat'l) |  | 4 | 1 | 1
9 | 1001J | QC5-2678 | QC8-5533 | QM4-4536 | 4 | 1 | 0
10 | 1001J | QC5-6187 | QC9-4151 |  | 5 | 1 | 0
11 | 1001J | QD1-2374 | QC8-2613 | QC7-5940 | 5 | 2 | 4
12 | 1001J | QD1-2375 | QC8-2614 | QC7-5951 | 5 | 2 | 5
13 | 1001J | QD1-2358 | QC8-2547 |  | 3 | 1 | 3
14 | 1001J | QD1-2366 | QC8-2578 |  | 3 | 1 | 0
15 | 1001J | QC5-6174 |  |  | 7 | 2 | 0
16 | 1001J | QC5-9312 |  |  | 30 | 1 | 0
17 | 1001J | QC5-9313 |  |  | 30 | 1 | 0
18 | 1001J | QC5-9301 |  |  | 30 | 1 | 0
19 | 1001J | QC5-9302 |  |  | 30 | 1 | 0
20 | 1002J | FE2-P911 |  |  | 1 | 2 | 14
21 | 1002J | FE3-6799 |  |  | 2 | 2 | 9
22 | 1002J | FE3-K645 |  |  | 15 | 2 | 0
23 | 1002J | FE3-L985 |  |  | 15 | 2 | 0
24 | 1002J | FE2-L238 |  |  | 3 | 2 | 1
25 | 1002J | FE3-7438 |  |  | 3 | 2 | 3
26 | 1002J | FE2-N591 | FL1-H130 |  | 5 | 2 | 9
27 | 1002J | FE2-L230 | FL1-A133 |  | 5 | 2 | 0
28 | 1002J | QC8-4391 | QC8-1084(change mat'l) |  | 15 | 2 | 2
29 | 1002J | QC8-4393 | QC8-1086(change mat'l) |  | 15 | 2 | 1
30 | 1002J | FE2-M001/M002 |  |  | 5 | 2 | 0/0
31 | 1002J | QC8-1080 |  |  | 1 | 2 | 0
32 | 1002J | QC8-1152 |  |  | 1 | 2 | 3
33 | 1002J | QC8-1153 |  |  | 2 | 2 | 2 (ใย bari)
34 | 1002J | QC4-9176 | QC8-1270(change mat'l) |  | 30 | 2 | 0
35 | 1002J | QC4-9447 | QC8-1271(change mat'l) |  | 30 | 2 | 0
36 | 1002J | QC5-9299 | QC7-5885 (Change Mat’l) |  | 30 | 2 | 0
37 | 1002J | QC5-9300 | QC7-5886(change mat'l) |  | 30 | 2 | 0
38 | 1002J | QC5-9296 | QC7-5891(change mat'l) |  | 30 | 2 | 0
Lot Size
1 = Run ทุกวัน
2 = วันเว้นวัน
3 = 3 Run 1 ครั้ง
4 = 4 Run 1 ครั้ง
5 = 5 Run 1 ครั้ง
7 = 7 Run 1 ครั้ง
15 = 4 Run 1 ครั้ง
30 = 4 Run 1 ครั้ง

## Slide 29
Summary Process Time of 1001T , 1002T
Detail Compare Time Operator at Cannot use Robot
HT-MFG2 Mold Equipment Budget Request
29